Model TPW-23 Oven and Cooker User

Contents

1. OVEN ELECTRONIC CARD	2

1.1 INTRODUCTION	2

1.1.1 Touch Buttons	2

1.1.2 Cooking Function Selection button	2

1.1.3 Temperature Adjustment button	3

1.1.5 Screen Symbols	4

1.2 USE	6

1.2.1 Switching ON	6

1.2.2 The Main Menu Screen and its items	7

1.2.3 Cooking	7

1.2.4 Alarm	15

1.2.5 Smart functions	16

1.2.6 Error Codes	21

1.2.7. Drawing of Connections	22

1.2.8. Electrical Connection Diagram	23

2. 30 CM BUILT-IN STOVE OVALDUAL - DOUBLE ELECTRONIC BOARD	24

2.1 Turning the Stove ON/OFF	24

2.2 Child Lock Function (Optional)	28

2.3 Error Codes and Recommendations for Solutions	31

2.4 Hotplate usage	32

2.5 Electric heating power	33

2.6 Maintenance and cleaning	34

# 1. OVEN ELECTRONIC CARD

## 1.1 INTRODUCTION

### 1.1.1 Touch Buttons

### 1.1.2 Cooking Function Selection button

Resides on the left hand side of the oven and the screen ( in some oven models,  its position may be exchanged with the Tempererature Adjustment button )  and serves to select the desired cooking function. As the big oven symbol with symbolized cooking function is flashing on the screen ( means you are allowed  to change the currently assigned cooking function ),  touching it up/down will bring the next/previous cooking function onto the screen.  The  cooking function appearing on the screen will be  accompanied by its default  assigned Temperature , flashing on the screen.

### 1.1.3 Temperature Adjustment Button

Resides on the right hand side of the oven and the screen ( in some models , its position is exchanged with the Cooking Function Selection  Button )  and serves to adjust the cooking Temperature.  As the Temperature assigned to the cooking  function is flashing,  touching up/down buttons will increase/decrease  the adjusted Tempereature in 5C ( 5F).

Cooking Function and Temperature Selection Touch Buttons

TCH-2B touch boards can be used instead of selection buttons. Every touching to appropriate button changes cooking function to the next one or changes temperature 5C (5F) steps.1.1.4 Touch Buttons

Switches the oven ON or OFF upon long press ( 1 sec )  , independent of the child lock. Any running program will be cancelled when turned OFF.

When scrolling through screen menus, pressing this button has the function of returning to the previous menu, at the end resulting in the idle screen.  Pressing this button during a running cooking program will pause, a long ( 2 sec ) press will cancel the program.

Serves to toggle between idle and main menu screens.  In some cases / screens, it serves as a shortcut key to access directly the related edit menu.

Used to scroll upwards within menu items or for increasing any numerical parameter on the screen during editing.  Long press during a cooking activates the RAPID HEAT UP function.

Used to scroll downwards within menu items or for decreasing any numerical parameter on the screen during editing. Long presses except being in any adjustment mode, will turn on and off the lamp.

Used for selecting a highlighted menu item or confirm any ( adjusted ) parameter visible on the screen or to start cooking or a cooking program with prev. adjusted parameters.

### 1.1.5 Screen Symbols

The symbols which may appear on your screen and their meanings are below

|  | TOP heating element |  | Turnspit |
| --- | --- | --- | --- |
|  | Grill heating element |  | Circular(Turbo) Fan (Opsiyonel) |
|  | Selected cooking function (left example is for a combination of top + bottom + fan elements) |  | Lamp |
|  | Bottom heating element |  | Defrost |
|  | KeepWarm |  | Tray position recommendation ( left example is for the mid position ) |
|  | Set Temperature and heating cycle indicator ( ) This symbol indicates the set Temperature level according to the scaling from 0-280C. During a heating cycle (heater relays on ), it will apear in red, otherwise in blue. |  | Thermometer Symbolises the oven cavity Temperature. The level of the interior fluid symbolization dynamically changes according to the measured cavity Temperature. It is scaled as 0C at the lowest, 280C at the top level. The color will be red when heating elements are active or the cavity Temperature is above 60C, otherwise it is blue. |
|  | Cooking Appears when a cooking is in progress |  | Waiting for the cooking start time Appears when a delayed cooking is programmed and waiting for the time to start cooking. |
|  | Rapid Heat Up |  | Alarm Appears steady when an alarm is or being set, flashes when the set alarm time has expired. |
|  | Cooking Menu |  | Settings Menu |
|  | Cooking Guide Menu |  | Auto Cooking. Appears steady during an automatic cooking,flashes upon its completion. |
|  | Manual Cooking |  | Screen Clock Apperance Menu |
|  | Start of Cooking |  | Language Selection Menu |
|  | Cooking Duration |  | Time of day Time of day / clock adjustment |
|  | End of Cooking |  | Date adjustment Menu |
|  | Elapsed cooking time |  | Sound Menu ( symbol on the left means all sound effects are on ) |
|  | Alarm Clock |  | Temperature Unit Selection Menu |
|  | Child Lock |  |  |

## 1.2 USE

### 1.2.1 Switching ON

The screen will be black and empty when the device is OFF.  By long ( 1 sec) pressing of the  button, the device is switched on, the screen lights up (  a temporary logo screen may appear depending on the software version ) and the idle screen will be visible. The oven controls are enabled now.  To switch the device OFF, a long press of the same button is required. In that case, any running cooking program will be cancelled.

INFO: When no cooking or cooking program is in progress, the brightness of the screen will be reduced automatically after 1 minute following  the last button press.

Mains Power Losses:

Your oven control will not be affected from mains power interrupts shorter than 2 minutes. Longer power losses will cause  the oven to get  OFF, any adjusted cooking or alarm will be cancelled. Upon power restore after a long loss of power, the device will be in idle mode when it was  ON , in OFF mode when it was OFF before the mains power interrupt .

INFO!  Upon first installation or after a power loss lasting  longer than 48 hours, the date and time of day settings will not be correct. Please set/correct  them using  the SETTINGS menu.

The idle Screen

The idle screen is defined as the screen appearance as no cooking program  is in progress and the time of day and date are shown.   Any of the symbols  ,  ,  or  ,  not related to cooking may also take place  on the idle screen .

Digital Screeen Clock     Analog             Screen Clock                When oven cavity Temperature > 60C

When the Temperature of the oven cavity is above 60C, the screen will appear as red on black.

INFO :  The symbol   appearing on the  bottom  right of the screen indicates that the,   button has a shortcut function to enter the cooking menu directly. The function and Temperature settings indicated on the screen will be the ones used in the last cooking performed before..

### 1.2.2 The Main Menu Screen and its items

|  | There are 4 main menu items: ‘ALARM‘,‘COOKING’ , ‘COOKING GUIDE’ and ‘SETTINGS’. The MAIN MENU screen can be accessed upon pressing the button when no cooking program is in progress . You can scroll through the 4 main menu items by pressing or buttons and select one by pressing . By pressing or , you can return to the idle screen. |
| --- | --- |

### 1.2.3 Cooking

Using the cooking menu,  you can start a manual cooking or  program  an  automatic cooking and run it.

Cooking Functions

Your oven has 11 or more cooking functions.  There might be additional available functions depending on the oven model.

| Display | Function Name | Recommended Temperature | Setting Range | Display | Function Name | Recommended Temperature | Setting Range | Display | Function Name | Recommended Temperature | Setting Range |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Static Cooking | 200C | 50C-250C |  | Bottom Cooking | 180C | 50C-250C |  | Top Cooking | 180C | 50C-250C |
|  | Small Grill | 250C | 50C-250C |  | Grill | 250C | 50C-250C |  | Small Grill + Fan | 200C | 50C-250C |
|  | Static + Fan | 200C | 50C-250C |  | Pizza | 200C | 50C-250C |  | Grill + Turnspit | 250C | 50C- 250C |
|  | Defrost | 20C | 20C-60C |  | Keep Warm | 80C | 60C-90C |  | Small Grill + Turnspit | 250C | 50C-250C |

Manual Cooking

It is a cooking type in which you select the cooking function and Temperature manually and terminate cooking manually after being sure the food is well cooked.

Press    as no cooking present and enter the main menu.  Select “COOKING” by pressing   . The screen will show the first cooking function and its assigned Temperature in a flashing manner.  (pressing directy  as the idle screen is visible is also available as a shortcut, in that case the last cooking parameters - function and Temperature – will be flashing)

Rotating the cooking function Selector button,  select the desired function. The assigned Temperature of this function will also appear on the screen..

Rotating the Temperature button, you may change the Temperature within allowed limits.

Press  to start cooking.  Cooking will last until manually stopped or the maximum allowed duration ( 10 hours ) have been elapsed.  In the latter case, an error code ( see Error Codes ) will be displayed on the screen.

Note:	The elapsed cooking duration will be shown  on the bottom  near  the symbol   in hours: minutes format.

Pause, Edit  or  Cancel  a Manual Cooking

During a manual cooking, pressing  will pause it ,  PAUSE will appear on the screen in a flashing manner.  An edit screen with flashing cooking function and Temperature is accessed.   Rotating the related buttons on both sides , the cooking function and Temperature can be changed.  Pressing  will resume manual cooking with the changes made if any.  Instead, you can also press  to access automatic cooking parameters.

At any time during manual cooking, by pressing  (  results in the idle screen ) or     ( screen will turn off ) for 2 seconds  , you may cancel  the  manual cooking.

Auto Cooking

In case of using automatic cooking, by programming  the cooking period and/or the cooking end time, cooking will be terminated  automatically and accordingly.

Auto Cooking / Instant start

Cooking will start immediately and will be automatically  terminated when the  defined cooking duration has elapsed.

- Follow the first 3 steps of manual cooking ( explained above ) to set the desired cooking function and Temperature.

- Press  to enter the cooking duration menu.

- Set the desired cooking duration using buttons  or  (maximum allowed cooking duration is 10 hours ). Press  to confirm your adjustment.  The screen will show the cooking end time.

- Press   to start auto cooking.  Cooking will  be automatically ended when the cooking duration has  elapsed.

Note: In the bottom  info  line of the screen , you will see the cooking start time,  the remaining cooking duration and the cooking end time.

Delayed Auto Cooking

You may also use your oven by defining a cooking end  (food ready ) time. In this case, cooking will not start immediately but after some delay. This delay is automatically calculated according to the end time setting you give in and the cooking duration. The end time ( food ready time ) cannot exceed the current time of day plus  23 hours 59 minutes.

- Follow the first 3 steps of auto cooking ( explained above ) to set the desired cooking function, Temperature and cooking duration.

- Press . The screen will show the end time.

- Set the desired cooking end time using  or  buttons ( maximum allowed cooking end time is current time + 23hours 59 minutes )

- Press  to start the delayed cooking program . Now , the control will wait until  the calculated cooking start time,  which is symbolized by    appearing on the screen.

In the example below,  it is explained how a previously entered  1h:15 min duration cooking is  delayed so that cooking will be terminated automatically at  12:50.  Since the current time of day is 10:30, the oven will wait until 11:35, at that time start cooking for 1 hour 15 minutes and automatically stop cooking at 12:50.

Note:  In the bottom line of the screen , you will see the cooking start time , cooking duration and the cooking end time.

Pause, Edit  or  Cancel  an Automatic Cooking :

During an Auto Cooking, pressing    will pause it,  PAUSE, cooking function and Temperature will start flashing.  Rotating the related buttons on both sides, the cooking function and Temperature can be changed.  .  You may also press  to enter the menus for editing the cooking duration and end time.  Pressing  will resume auto- cooking with the changes made if any.

At any time during auto-cooking, by pressing  (  results in the idle screen ) or     ( screen will turn off ) for 2 seconds  , you may cancel  the cooking . The cooking program will be erased.

Note: On the bottom line of the Follow the first 3 steps of manual cooking ( explained above ) to set the desired cooking function and Temperature.

Cooking guide

Using the Cooking Guide menu,  you can select one food type among a variety.  The most suitable cooking function, Temperature, Cooking Duration will be automatically set . You will also be advised a suitable tray position.

- Press   as no running cooking program, and access the main menu. Select ‘Cooking Guide’  using buttons  or   and press  . The first type of food in memory and the suggested tray position will be shown on the screen.

- Using the  or   buttons  (or by rotating the Function Selector Button ) , you may scroll through all available food types. Press   when the desired food type is on the screen.

- For some type of foods,  the control will ask you if  your food to be cookedis a single piece or multi pieces ( e.g  a big piece of meat or  sliced meat /steak ). Using   or  , select the correct match and press  to confirm.

- The weight of the food to be cooked might be asked for some food types.  Give in the right weight ( correct the default weight appearing if necessary ) using  or   and confirm with .

- The screen will show all parameters of the cooking you are about to start. The set oven Temperature will be flashing and can be changed within allowed limits rotating the Temperature button.

- Pressing  will start cooking with the parameters seen on the screen including the automatically set cooking duration and end time.  Before pressing , you may edit those two parameters by pressing  and entering the edit menu . Editing is done as explained before in the AUTO COOKING paragraph before  (Please note that the cooking duration is only allowed to be changed within some limits) .

Pause, Edit  or  Cancel  a  Cooking :

During Cooking,  pressing    will pause it,  PAUSE  and Temperature  will start  flashing. Rotating the related button, Temperature can be changed.  You may also press  to enter the menus for editing the cooking duration and end time.  Pressing  will resume auto- cooking with the changes made if any.

At any time during auto -cooking, by  pressing  (  results in the idle screen ) or     ( screen will turn off ) for 2 seconds  , you may cancel  the cooking . The cooking program will be erased. .

Automatic End of a Cooking

Any  cooking except manual,  will end automatically when the programmed  cooking duration has elapsed.  The screen will show the ‘cooking finished’ indication, AUTO symbol will be flashing and a buzzer tone is heard. Press    to confirm you received the message and stop it,  the idle screen will be visible now.

INFO:  The Cooking Function and Temperature setting of the last cooking will be memorized.  Direct Access to the cooking menu with those parameters is possible when   appears nearby.

### 1.2.4 Alarm

You may use the Alarm function independent of the cooking functions.  The alarm will sound after the adjusted duration has elapsed or the adjusted time of day has been reached.

Press  .  This will result in the main menu screen if no cooking or cooking program is running, select ALARM using buttons  or    and confirm with . The alarm duration menu will appear. If a cooking or cooking program was running, this screen will appear directly upon pressing .

Using buttons  and    , adjust the alarm duration in terms of hours: seconds. Note that, the time of day the alarm will be activated ( calculated according to the duration being programmed ), is also indicated on the bottom right of the screen, nearby the  symbol.  After completing your adjustment, press  to confirm.

The remaining time for  the alarm will be indicated on the top of the screen if less than 10 minutes,  in minutes : seconds format, nearby the  symbol.  If more than 10 minutes, the time of day the alarm will be active is indicated instead, nearby the  symbol.

Auto end or Cancelation of an Alarm:

To cancel any running alarm countdown, the duration has to be set to zero following the steps above.

When the programmed alarm time has been reached / programmed duration has expired, the buzzer will sound and   0:00 will be flashing on the screen. Any button press will stop the buzzer, whereas only pressing  will clear up the screen resulting  in the idle screen.

### 1.2.5 Smart functions

The Child Lock

In order to prevent unintended  button  presses , you may use the child lock function. To activate, press both  and    simultenously for 2 seconds, when not beeing in any  adjustment mode. The symbol   will appear on the left top of the screen.

When the child lock is active, only button  will be functional . By  long pressing    you can  turn the control ON or OFF.  All other touch keys will be  inactive.

As the child lock is active,  any button press except    will result in a warning message shown below. To disengage the child lock, press   both   and    buttons for 2 seconds.

Rapid Heat Up

This tool is usefull for heating up the oven rapidly to the set Temperature  by temporarily activating  convectional   heating ( circular heating elements and turbo fan ) . Those additional heating elements will automatically be deactivated when the desired cavity Temperature has been reached.

As cooking is running ( after having started )  , pressing    for 2 seconds will activate this function. The rapid heat up symbol   will appear on the right of the cooking symbol .

To cancel any running  rapid heat up function,  pressing  for  2 seconds is required.

The rapid heat up function is automatically cancelled when the oven cavity Temperature reaches the set value,    symbol will disappear.

Note: Rapid Heat Up cannot be activated during any  grill function  or if the difference between set and  actual Temperature is less than 50C or the set Temperature is below 100C in other functions

Lamp ON/OFF

When not in any adjustment menu, pressing    for 2 seconds will toggle the lamp off and on.

Switching the Lamp OFF:

Switching the Lamp ON:

When the Lamp is ON, the lamp symbol on the screen will appear colored, when OFF grey.

Note: when entering the cooking menu lamp light up automatically. if user starts cooking lamp remains lit. If desired, the lamp can be turned off by pressing the  button for 2 seconds.

Settings

Using this menu, you may adjust the time of day, date, language, screen clock ( digital or analog ) , sound preferences and  the Temperature unit  to be used.

Press   as no running cooking program, and access the main menu, select  SETTINGS using buttons    or     and press    .   The first menu on the screen will be the time of day.  To  make adjustments on the current menu on the screen, press  , to access  other menus, scroll with   or    . Press , when the menu to be adjusted appears on the screen.

INFO: In case of a running cooking or cooking program , the Settings  menu cannot be accesed.

Time of Day

Following the steps below, the time of day can be adjusted.

As seen above , you can select any of  24 or 12 hour formats.

INFO: In case of an alarm countdown, time of day menu cannot be accessed.

Date

Following the steps below, the date can be adjusted.

Sounds

Selecting and confirming  , the buzzer sound will only be active upon any alarm and/or cooking end. Selecting  will  activate all other warning tones available additionally.

Temperature Unit

Any of the units Celcius or Fahrenheit can be selected as explained below.

Screen Clock

The clock indication on the idle screen may be selected as digital or analog as explained below.

Language

Any of the available kanguages may be selected as explained below.

INFO :  After completing an adjustment , the  adjusted menu item will appear on the screen . You may select another item to be adjusted using buttons  or    and confirm with  or return to the main menu screen by pressing   .

### 1.2.6 Error Codes

Any error preventing normal operation  will be displayed on the screen . In that case, any running cooking or cooking program will be cancelled.  The message will remain on the screen until   is pressed , even if the error has been recovered.

| Error Code | Explanation |
| --- | --- |
| Error 1 | Temperature Sensor Error The connector of the sensor may be loose or disconnected. Temperature sensor malfunction . Power Module malfunction |
| Error 2 | User Module Temperature limit exceeded The ambient Temperature of the user module is > 85C. Cooling Fan malfunction . User module malfunction |
| Error 3 | User Module Temperature Limit Sensor Error User module malfunction |
| Error 6 | Real Time Clock Error The real time clock IC on the user module is defect. |
| Error 8 | Power Section Error ( oven gets not heated or does not cool down ) Loose heating element connection Power Module malfunction |
| Error 9 | Frequency Error The crystal oscilator of the real time clock is defect. |

1.2.7. Drawing of Connections

### 1.2.8. Electrical Connection Diagram

# 2. 30 CM BUILT-IN STOVE OVALDUAL - DOUBLE ELECTRONIC BOARD

|  | Upper cooking area selection key |
| --- | --- |
|  | Lower cooking area selection key |
|  | Special function selection key |
|  | Plus key |
|  | Minus key |
|  | On / OFF key |
|  | Temperature display icon |

## 2.1 Turning the Stove ON/OFF

Note: Unit becomes operational within 1 second after it is plugged to the mains. All LEDs and displays illuminate for 1 second.

|  | Unit is turned on by pressing the key. The symbol is displayed on all displays. (See Fig. 1) |
| --- | --- |
| Figure 1 |  |

|  | If the temperature of the glass over the hobs is above + 60°C, and icons are displayed on the display of the relevant successively. ( = 0.5 seconds, = 0.5 seconds) (see Fig. 2) |
| --- | --- |
| Figure 2 |  |

|  | Unit is turned off by pressing the key. (see Fig. 3) You may turn off the unit by pressing the key even if the child lock is active. |
| --- | --- |
| Figure 3 |  |

WARNING: Electronic components remain active for 20 seconds. If there is no cooking level within this period, unit switches to ‘‘off mode’’ automatically with a signalling sound.

Residual Heat Display

|  | If the icon on the display of the stove is illuminated, this means that the relevant hob is still hot. It may be used for heating a small amount of food. (See Fig. 4) WARNING: Residual heat display is not illuminated and thus it does not warn the user against heat in case of a power outage |
| --- | --- |
| Figure 4 |  |

WARNING: Residual heat display of each cooking area remains active until the measured glass temperature is below + 60 °C.

Turning the Stove Cooking Areas ON

|  | 1. Turn the stove on by pressing the button. (See Fig. 5) |
| --- | --- |
| Figure 5 |  |

|  | 2. Press the relevant hob selection key. The icon shall be displayed in the relevant hob when you touch for the first time. (See Fig. 6) |
| --- | --- |
| Figure 6 |  |

|  | 3. Power level of the relevant hob may be set from 1 to 9 using the and the keys or from to 9 as per the option of the stove. (See Fig. 7) |
| --- | --- |
| Figure 7 |  |

WARNING: If the hob selected is hot, icon shall be displayed instead of  icon after the selection is made.

Keep Warm Function  (Optional)

Keep warm function keeps the cooked food placed on a cooking area warm. The selected hob is operated with a lower power in this function. Keep warm function is also a cooking level.

To activate the keep warm function

|  | 1. Turn the stove on by pressing the button. (See Fig. 8) |
| --- | --- |
| Figure 8 |  |

|  | 2. Press the relevant hob selection key once. The icon is displayed when you touch for the first time. (See Fig. 9) |
| --- | --- |
| Figure 9 |  |

|  | 3. Then, press the key once. The icon shall be displayed in the relevant hob with this touch. (see Fig. 10) Thus, the keep warm shall be activated. |
| --- | --- |
| Figure 10 |  |

Turning the Stove Cooking Areas Off:

|  | 1. You may turn the stove off by pressing the button. (See Fig. 11) |
| --- | --- |
| Figure 11 |  |

|  | 2. Using the and keys, bring the temperature on all hobs to. (see Fig. 12) Stove shall be turned off by itself after 20 seconds. |
| --- | --- |
| Figure 12 |  |
|  | 3. If any hob is still hot after 20 seconds, symbol is displayed until the temperature of the relevanthob becomes lower than +60 °C. (see Fig. 13) No icon is displayed after the stove is turned off if the relevant hob is not hot. |
| Figure 13 |  |

## 2.2 Child Lock Function (Optional)

To activate the child lock

|  | 1. Press upper hob selection key ( ) and plus key ( ) simultaneously, you shall hear a short warning signal at this time. (see Fig. 14) Then, remove your fingers from the stove control panel. |
| --- | --- |
| Figure 14 |  |
|  | 2. Press the upper hob selection key ( ) again. (See Fig. 15) |
| Figure 15 |  |
|  | 3. The child lock is activated at this time and the icon is displayed on all hobs to indicate this condition. (see Fig. 16) The and icons are displayed alternatively if any hob is hot. |
| Figure 16 |  |

To deactivate the child lock until the stove is turned off

|  | The icon is displayed on all displays when the stove is on and the child lock is active. (see Fig. 17) The and icons are displayed alternatively if any hob is hot. You may turn the stove on or off with the key only. |
| --- | --- |
| Figure 17 |  |
|  | Press upper hob selection key ( ) and plus key ( ) simultaneously. (see Fig. 18) You shall hear a short warning signal at this time. Then, remove your fingers from the stove control panel. |
| Figure 18 |  |

|  | 3. The icon is displayed on all displays. (see Fig. 19) The and icons are displayed alternatively if any hob is hot. |
| --- | --- |
| Figure 19 |  |

WARNING: Child lock is deactivated until the stove is turned off only with the steps performed in this section. In other words, child lock shall be activated again if the unit is turned off and on again. Thus, the child lock shall be activated whenever the stove is turned off and on.

To activate the child lock completely

|  | 1. The icon is displayed on all displays when the stove is on and the child lock is active. (see Fig. 20) The and icons are displayed alternatively if any hob is hot. You may turn the stove on or off with the key only. |
| --- | --- |
| Figure 20 |  |
|  | 2. Press upper hob selection key ( ) and plus key ( ) simultaneously. (see Fig. 21) You shall hear a short warning signal at this time. Then, remove your fingers from the stove control panel. |
| Figure 21 |  |
|  | Press the key again. (see Fig. 22) This shall be performed right after the 2nd step. Child lock is deactivated permanently. In other words, child lock shall continue to be deactivated even if the unit is turned off and on again. |
| Figure 22 |  |

|  | Unit switches to stand-by mode after these procedures. However, the icon shall be displayed in case of a hot hob even if the unit switches to stand-by mode. (See Fig. 23) |
| --- | --- |
| Figure 23 |  |

WARNING: Child lock shall be deactivated in case of a power outage.

Special Function Selection Key

Special function selection key controls the double heater. When the double heater is selected for cooking, both hobs of this heater are activated. You may select one cooking area of the double heater by pressing the special function selection key. Touch the special function selection key again to activate both cooking areas of the heater.

|  | A point ( ) icon is displayed beside the cooking level of the relevant hob when both hobs of the double heater are active. (See Fig. 24) |
| --- | --- |
| Figure 24 |  |

|  | Cooking level is displayed by itself without a point ( ) icon when a single hob of the double heater is activated by touching the special function selection key. (See Fig. 25) |
| --- | --- |
| Figure 25 |  |

## 2.3 Error Codes and Recommendations for Solutions

Error codes, their probable causes and recommendations for solutions are provided in the chart below.

WARNING: The chart below is applicable for all models

| .Error Code | Error Description | Potential Cause for Error | Clearing Error |
| --- | --- | --- | --- |
| ER 03 & continuous signal sound | Constant use of buttons; control unit is disrupted after 10 seconds. | Water or cooking utensils on the glass over the control unit. | Clean the operating surface of the stove. |
| ER 20 | Flash fault. | ^ C error. | Replace the electronic board. |
| ER 21 | Excessive temperature. | The ambient temperature for electronics is too high. | Allow the cooking surface to cool down. Check the temperature verification of the control unit. |
| ER 22 | Key evaluation fault. Control unit is turned after 3.5 – 7.5 seconds. | Short circuit or error in detection of keys. | Replace the electronic board. |
| ER 31 | Configuration data is incorrect. | --- | New configuration is required. |
| ER 36 | Temperature sensor error. | Short circuit or electronic board turns off. | Replace the electronic board. |
| ER 40 | Power supply is too low to turn on the appliance | Primary PTC is too hot. | Disconnect the stove from power supply system. |
| ER 47 | Communication error between the electronic board configuration and the heaters. | No communication or faulty communication. | Make sure that the connection cable is connected correctly and functionally. |
| U 400 | Incorrect connection. | Control unit is connected incorrectly. | Connect the stove to correct mains voltage. |

WARNING: If the device is operated at maximum level for too long, it can turn off automatically. This is an ordinary measure for safety of the device.

## 2.4 Hotplate usage

You can use the electric cooker, by selecting the desired level through remote panel button. The power of the cooker according to the level is given in the table below.

|  | LEVEL 1 | LEVEL 2 | LEVEL 3 | LEVEL 4 | LEVEL 5 | LEVEL 6 |
| --- | --- | --- | --- | --- | --- | --- |
| 80 mm | 200 W | 250 W | 450 W | --- | --- | --- |
| 145 mm | 250 W | 750 W | 1000 W | --- | --- | --- |
| 180 mm | 500 W | 750 W | 1500 W | --- | --- | --- |
| 145 mm Speed | 500 W | 1000 W | 1500 W | --- | --- | --- |
| 180 mm speed | 850 W | 1150 W | 2000 W | --- | --- | --- |
| 145 mm | 95 W | 155 W | 250 W | 400 W | 750 W | 1000 W |
| 180 mm | 115 W | 175 W | 250 W | 600 W | 850 W | 1500 W |
| 145 mm Speed | 135 W | 165 W | 250 W | 500 W | 750 W | 1500 W |
| 180 mm Speed | 175 W | 220 W | 300 W | 850 W | 1150 W | W |

## 2.5 Electric heating power

|  | LEVEL 1 | LEVEL 2 | LEVEL 3 | LEVEL 4 | LEVEL 5 | LEVEL 6 | LEVEL 7 | LEVEL 8 | LEVEL 9 | Max. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ø 140 mm Commutator | 130 W | 206 W | 350 W | 500 W | 850 W | 1200 W | --- | --- | --- | --- |
| Ø 180 mm Commutator | 180 W | 470 W | 790 W | 850 W | 1230 W | 1700 W | --- | --- | --- | --- |
| Ø 180 mm Regulator | 1800 W | 1800 W | 1800 W | 1800 W | 1800 W | 1800 W | 1800 W | 1800 W | 1800 W | --- |
| Ø140/250 mm Ovaldual | 1000 W | 1000 W | 1000 W | 1000 W | 1000 W | 1000 W | 1000 W | 1000 W | 1000 W | 1800 W |
| Ø120/180 mm Double | 700 W | 700 W | 700 W | 700 W | 700 W | 700 W | 700 W | 700 W | 700 W | 1700 W |

The diameter of the cookware needs to be minimum 120 mm.

## 2.6 Maintenance and cleaning

Before cleaning the cooker please unplug it from electricity. If the cooker is hot please wait until it is cool.

1.	Your cooker must be cleaned and maintained regularly to ensure a long economic life.

2.	Do not clean the cooker with hard tools such as hard brushes, dishwasher wire or knives. Do not use abrasives, scourers, acidic substances or detergents.

3.	After wiping the parts of your stove with a soapy cloth, rinse, then dry thoroughly with a soft cloth.

4.	Clean glass surfaces with special glass cleaning agents. Do not use abrasive cleaners or sharp metal scrapers when cleaning glass surfaces, as scratching and breaking of glass surfaces may result.

5.	Do not clean the cooker with steam cleaners.

6.	Never use flammable materials such as acid, thinner or gas when cleaning your hob.

7.	Do not wash any cooker parts in the dishwasher.

8.	Vinegar, lemon, salt, cola and similar acid and alkaline spills on your cooker should be cleaned quickly.

9.	Over time, it may be difficult to turn the cooker buttons or turn them at all, in this case the buttons need to be replaced. Replacement must only be carried out by authorized service.

Figure 3

# Text boxes

TR

When the oven cavity Temperature is below 60C

When the oven cavity Temperature is above 60C .

The warning message will disappear after 10 seconds if key lock is not disengaged.